Deriving servo angles from local coordinates of toe	ver 6

Task: Given the location of the toe at point T = (Tx, Ty, Tz), find the servo rotation angles for the hip Rh, knee Rk and ankle Ra with angles expressed in degrees.

General approach: Find the coordinates of the ankle (Ax, Ay, Az) and from there, calculate the angles.

Finding the hip angle is straight forward. Looking down from above, the leg’s projection in the local xz plane is a straight line that is the hypotenuse of a right angled triangle with the X axis, with the hip angle between these 2 lines. Therefore:
   tan(Rh) = Tz/Tx, or Rh = arctan(Tz/Tx) // in spreadsheet & program, ATAN2(y,x) function, as ATAN2(Tz, Tx), different arg order

Based on this, we can use Rh in calculating the ankle coordinates.

To reduce the 3D problem to 2D, envision rotating the hip servo so its angle is zero, and the leg is sticking straight sideways.

Viewing from the top again, we have a plane that’s like (x,y) coordinates but in our case, the traditional x axis is the local z axis, and the traditional y axis is the local x axis, negated.

The formula for rotating a 2D vector (x,y) through a counter clockwise angle beta is:
   (x,y) --> ( x*cos(beta) - y*sin(beta) , x*sin(beta) + y*cos(beta) )

to apply this to the path of the toe in our case, we have to:

- account for our angle being clockwise.
Although the rotation of the hip servo Rh is positive when going counter clockwise, the rotation we’re doing to the toe is opposite to that, clockwise. We negate it to change direction and get -Rh counter clockwise.
Our rotation formula requires that the angle be expressed as counter clockwise, so for beta in the formula, we’ll use -Rh.

- account for our different coordinates
Using the pivot point as the origin (which fortunately is the origin of the local coordinate system as well), to rotate the toe vector, we get:
     traditional x value for toe vector is Tz, the toe position’s local z coordinate
     traditional y value for toe vector is -Tx, the toe position’s local x coordinate negated.

if (Ux, Uy, Uz) represents the rotated position of the toe, then:

   Ux = the rotated toe point’s y coordinate, negated (local positive x axis is in direction of traditional negative y axis)
        = -1 * (x * sin(beta) + y * cos(beta) ) using traditional coordinates in rotation formula
        = -1 * (Tz * sin(-1*Rh) + (-Tx) * cos(-1*Rh) ) using the equivalent in local coordinates
        = Tx * cos(-1*Rh) – Tz * sin(-1*h) [0]

   Uy = Ty // our rotation doesn’t change the y coordinate of any points

   Uz = 0 // we selected our rotation to give this

Now let’s look at the plane where z = 0, containing our rotated leg sticking out sideways.

The ankle lies on a circle of radius 7.5 cm (body shin measurement, or BS) , centred on the knee which is 2.5 cm (body thigh measurement, or BT) from the origin,
       above the hip servo, at y=0.
It also lies on a circle with radius 11 cm (body measurement diagonally across foot from ankle to toe, or BF), centred on the toe, at (Ux, Uy, Uz)

The formula for a circle is ( x - Xc)^2 + (y - Yc)^2 = r^2 where (Xc,Yc) is the center, and r is the radius

The equation for the first circle is:
     (x - BT)^2 + (y - 0)^2 = BS^2
     x^2 -2*BT*x + BT^2 + y^2 = BS^2 [1]

for the second circle:
    (x - Ux)^2 + (y - Uy)^2 = BF^2
    x^2 -2*x*Ux + Ux^2 + y^2 -2*y*Uy + Uy^2 = BF^2 [2]
   (y - Uy)^2 = BF^2 - (x - Ux)^2, y = +/- sqrt( BF^2 - (x - Ux)^2 ) + Uy [3]

subtracting equation [2] from equation [1]...
x^2 - 2*BT*x + BT^2 +y^2 -x^2 + 2*x*Ux -Ux^2 -y^2 +2*y*Uy -Uy^2 = BS^2 - BF^2

x^2(1-1) +x(-2BT+2*Ux) +y^2(1-1) +y(2*Uy) + BT^2 -Ux^2-Uy^2 = BS^s - BF^2

x(-2BT+2*Ux) +y(2*Uy) + BT^2 - Ux^2 - Uy^2 = BS^s – BF^2

y = (BS^2 – BF^2 + Ux^2 + Uy^2 – BT^2 +x*(2BT -2Ux) ) / (2 * Uy) [3]

substituting y as defined by [3] back into equation [1]

     x^2 - 2 * BT*x + BT^2 + y^2 = BS^2 [1]

     x^2 - 2 * BT*x + BT^2 + ( (BS^2 – BF^2 + Ux^2 +Uy^2 – BT^2 + x*(2*BT – 2*Ux) ) / (2 * Uy) )^2– BS^2 = 0

     since BS, BF, Ux, Uy and BT are fixed constants for given toe position, we can treat algebraic combinations of them as a single coefficient
        thus we define C1 = BS^2 – BF^2 + Ux^2 + Uy^2 - BT^2
        and C2 = 2*BT – 2*Ux

     x^2 – 2*BT*x + BT^2 + ( C1 + x* C2 )^2 - BS^2 = 0
        ---------------------
        (2*Uy)^2

     x^2 – 2*BT*x + BT^2 + ( C1^2 + 2*C1*x*(C2) + x^2*C2^2) - BS^2 = 0
        --------------------------------------------
        (2*Uy)^2

     x^2*(1 + C2^2 ) + x*( -2*BT + 2*C1*C2 ) + ( BT^2 + C1^2 - BS^2 ) = 0 [4]
        --------- ----------- ---------
        4*Uy^2 4*Uy^2 4*Uy^2
which is a quadratic equation in x, of the form ax^2 +bx + c = 0, with solutions ( - b +/- SQRT( b^2 - 4*a*c) / (2*a) //note the +/-, which gives 2 solutions (sometimes)

a = 1 + C2^2/(4*Uy^2)

b = -2*BT + (2*C1*C2)/(4*Uy^2)

c = BT^2 + C1^2/(4*Uy^2) – BS^2

where
C1 = BS^2 – BF^2 + Ux^2 + Uy^2 -BT^2
C2 = 2*BT – 2*Ux

BS = body’s shin length
BF = body’s foot length (diagonal from ankle to toe)
BT = body’s thigh length
Ux = toe’s local X coordinate when projected onto local XY plane
Uy = toe’s local Y coordinate when projected onto local XY plane
Rh = hip rotation angle, positive is counterclockwise seen from above

   BTOA = Body’s Toe Offset angle, approximately 17 degrees
   BTOD = Body’s Toe Offset Distance, approximately 3.2 cm

In the general case, equation [4] gives 2 possible values for x due to the +/- choice. Equation [1] implies there are 2 possible y values for each, but equation [3] implies there is just one. Having 2 overall solutions seems appropriate, since the circles centred at the toe and the knee intersect in at most 2 points.

( Bring on the spreadsheets. Warning: spreadsheet ATAN2 function has different arg order than C++ )

So, when the dust settles we have possible values for (x,y), the local coordinates for the ankle. One corresponds to the choice of “plus” in the quadratic solution, designated by a “P” in spreadsheet variable names, and “M” represents the choice of minus. In each case, equation (3) is used to derive a single value for y.

The knee angle Rk is straightforward to calculate once we know that the ankle is (x, y):
    Rk = arctan( (y)/ (x - BT) ) // note that the knee is horizontally displaced from the origin by the thigh, thus the (x – BT) in the formula

The angle at the ankle is complicated because the toe is not in line with the servo’s zero position, but is about 17 degrees (Body Toe Offset Angle = BTOA) from it, away from the robot’s chassis. It also gets moved by the knee rotation.

If we temporarily ignore the offset , we can calculate the ankle angle R’a using either it’s arcsin or arctan function:
      R’a = arcsin( (Ux – x) / BF ) , or
      R’a = arctan( Ux – x) / ( y – Uy) )

This angle is composed of the BTOA 17 degree offset, the contribution due to knee rotation which is -ve, and the ankle rotation..
Thus Ra = R’a – 17 degrees - (-Rk)
        = arctan( Ux – x) / ( y – Uy) ) - BTOA + Rk